## Slide 1
Computer Vision / L476 board
Step Motor Control (x2)
  Step Motor Driver – TMC2100
RF data transmission
  RN41/42 – Evaluation Board XV
Position sensor SEN0239 (x3)
Light control (x3 – R / G / B)
Control of computer vision bench / Dobot conveyor
Functions
Based on Nucleo L476RG board
PROJECT VERSION

## Slide 2
Morpho Droit / Nucléo
Digital Output
Digital Input
Analog Input
PC_9
PB_8
PB_9
PA_6 / MISO
PA_7 / MOSI
D10 / CS
PB_3
PB_5
PB_13
PB_14
PB_2
PB_1
PA_10
D1
D0
PB_4
PB_10
PA_8
PA_9
PC_7
PA_5 / SCK
GND
PB_15
AGND
PC_4
GND
PB_11
PA_11
PB_12
PA_12
AVDD
U5V
PC_8
PC_6
PC_5
Morpho Gauche / Nucléo
PC_10
PC_12
PA_13
PA_14
PA_15
PH_1
PH_0
PA_1
PA_0
PC_2
PC_3
PC_15
PC_14
PC_13
PB_7
PB_0
GND
PC_11
PD_2
E5V
GND
3.3V
5V
GND
Vin
A2
PC_1
PC_0
GND
TX
RX
RESET_N
GPIO2_STATUS
nRF24 / SCK
nRF24 / MISO
nRF24 / MOSI
nRF24 / IRQ
nRF24 / CSN
nRF24 / CE
Not Used
CAPT 1
CAPT 2
CAPT 3
ECLAIR 3
ECLAIR 2
ECLAIR 1
Analog Output
V_OUT_REF
POUSS. 2
POUSS. 3
POUSS. 1
LED 1
LED 2
MOT1_STEP
MOT1_DIR
MOT1_EN
MOT1_CFG1
MOT1_CFG2
MOT1_CFG3
MOT1_STEP
MOT2_DIR
MOT2_STEP
MOT2_EN
Computer Vision / L476 board
Control of computer vision bench / Dobot conveyor

## Slide 3
Nucleo Board
TMC2100 – Step Motor Driver
Step Motor Driver / Motor 1 / TMC2100
TMC2100 / Motor1
GND
3.3V
PB_3
PB_13
PB_14
PB_1
PA_10
PB_15
PC_4
MOT1_STEP
MOT1_DIR
MOT1_EN
MOT1_CFG1
MOT1_CFG2
MOT1_CFG3
MOT1_STEP
PWM
MBED6 Library : https://github.com/IOGS-LEnsE-embedded/MBED6_SupOpLibraries/tree/main/TMC2100
A2
V_OUT_REF
Digital Output
Digital Input
Analog Input
Not Used
Analog Output

## Slide 4
Nucleo Board
nRF24 – RF transmission
nrF24L01 module for RF data transmission
PA_5/ SCK
nRF24L01 / RF
CLK
PA_7 / MOSI
MOSI
MISO
PA_6 / MISO
SPI
PC_7
CSN
CE
PA_8
PA_9
IRQ
GND
3.3V
MBED6 Library : https://github.com/IOGS-LEnsE-embedded/MBED6_SupOpLibraries/tree/main/nRF24
Digital Output
Digital Input
Analog Input
Not Used
Analog Output